## Slide 1: Complete Memory Addressing Modes
Remember, the addresses used for accessing memory in mov (and other) instructions can be computed in several different ways
Most General Form:
D(Rb,Ri,S) Mem[Reg[Rb] + S*Reg[Ri] + D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of the 8/16 integer registers
  Ri: Index register: Any, except for %esp or %rsp
    Unlikely you’d use %ebp, either
  S: Scale: 1, 2, 4, or 8 (why these numbers?)
Special Cases: can use any combination of D, Rb, Ri and S
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]
Notes: See figure 3.3 in textbook

## Slide 2: Address Computation Examples
%edx
%ecx
0xf000
0x100
Expression | Address Computation | Address
0x8(%edx) |  | 
(%edx,%ecx) |  | 
(%edx,%ecx,4) |  | 
0x80(,%edx,2) |  | 
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(,Ri,S) Mem[S*Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]
D(Rb) Mem[Reg[Rb] +D]
0xf000 + 0x8 0xf008
0xf000 + 0x100 0xf100
0xf000 + 4*0x100 0xf400
2*0xf000 + 0x80 0x1e080

## Slide 3: Address Computation Instruction
leal Src,Dest
  Src is address mode expression
  Set Dest to address computed by expression
    (lea stands for load effective address)
  Example: leal (%edx,%ecx,4), %eax
Uses
  Computing addresses without a memory reference
    E.g., translation of p = &x[i];
  Computing arithmetic expressions of the form x + k*i
    k = 1, 2, 4, or 8

## Slide 4: Some Arithmetic Operations
Two Operand (Binary) Instructions:
  Format Computation
  addl Src,Dest Dest = Dest + Src
  subl Src,Dest Dest = Dest - Src
  imull Src,Dest Dest = Dest * Src
  sall Src,Dest Dest = Dest << Src Also called shll
  sarl Src,Dest Dest = Dest >> Src Arithmetic
  shrl Src,Dest Dest = Dest >> Src Logical
  xorl Src,Dest Dest = Dest ^ Src
  andl Src,Dest Dest = Dest & Src
  orl Src,Dest Dest = Dest | Src
Watch out for argument order! (especially subl)
No distinction between signed and unsigned int (why?)

## Slide 5: Some Arithmetic Operations
One Operand (Unary) Instructions
  incl Dest Dest = Dest + 1
  decl Dest Dest = Dest - 1
  negl Dest Dest = -Dest
  notl Dest Dest = ~Dest
See textbook section 3.5.5 for more instructions: mull, cltd, idivl, divl

## Slide 6: Using leal for Arithmetic Expressions
int arith
(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}
arith:
pushl %ebp
movl %esp,%ebp
movl 8(%ebp),%eax
movl 12(%ebp),%edx
leal (%edx,%eax),%ecx
leal (%edx,%edx,2),%edx
sall $4,%edx
addl 16(%ebp),%ecx
leal 4(%edx,%eax),%eax
imull %ecx,%eax
movl %ebp,%esp
popl %ebp
ret
Body
Set
Up
Finish

## Slide 7: Understanding arith
int arith
(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}
movl 8(%ebp),%eax # eax = x
movl 12(%ebp),%edx # edx = y
leal (%edx,%eax),%ecx # ecx = x+y (t1)
leal (%edx,%edx,2),%edx # edx = y + 2*y = 3*y
sall $4,%edx # edx = 48*y (t4)
addl 16(%ebp),%ecx # ecx = z+t1 (t2)
leal 4(%edx,%eax),%eax # eax = 4+t4+x (t5)
imull %ecx,%eax # eax = t5*t2 (rval)
y
x
Rtn adr
Old %ebp
%ebp
0
4
8
12
Offset
Stack
•
•
•
z
16

## Slide 8: Understanding arith
int arith
(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}
movl 8(%ebp),%eax # eax = x
movl 12(%ebp),%edx # edx = y
leal (%edx,%eax),%ecx # ecx = x+y (t1)
leal (%edx,%edx,2),%edx # edx = y + 2*y = 3*y
sall $4,%edx # edx = 48*y (t4)
addl 16(%ebp),%ecx # ecx = z+t1 (t2)
leal 4(%edx,%eax),%eax # eax = 4+t4+x (t5)
imull %ecx,%eax # eax = t5*t2 (rval)
y
x
Rtn adr
Old %ebp
%ebp
0
4
8
12
Offset
Stack
•
•
•
z
16

## Slide 9: Understanding arith
int arith
(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}
movl 8(%ebp),%eax # eax = x
movl 12(%ebp),%edx # edx = y
leal (%edx,%eax),%ecx # ecx = x+y (t1)
leal (%edx,%edx,2),%edx # edx = y + 2*y = 3*y
sall $4,%edx # edx = 48*y (t4)
addl 16(%ebp),%ecx # ecx = z+t1 (t2)
leal 4(%edx,%eax),%eax # eax = 4+t4+x (t5)
imull %ecx,%eax # eax = t5*t2 (rval)
y
x
Rtn adr
Old %ebp
%ebp
0
4
8
12
Offset
Stack
•
•
•
z
16

## Slide 10: Understanding arith
int arith
(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}
movl 8(%ebp),%eax # eax = x
movl 12(%ebp),%edx # edx = y
leal (%edx,%eax),%ecx # ecx = x+y (t1)
leal (%edx,%edx,2),%edx # edx = y + 2*y = 3*y
sall $4,%edx # edx = 48*y (t4)
addl 16(%ebp),%ecx # ecx = z+t1 (t2)
leal 4(%edx,%eax),%eax # eax = 4+t4+x (t5)
imull %ecx,%eax # eax = t5*t2 (rval)
y
x
Rtn adr
Old %ebp
%ebp
0
4
8
12
Offset
Stack
•
•
•
z
16

## Slide 11: Observations about arith
int arith
(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}
movl 8(%ebp),%eax # eax = x
movl 12(%ebp),%edx # edx = y
leal (%edx,%eax),%ecx # ecx = x+y (t1)
leal (%edx,%edx,2),%edx # edx = y + 2*y = 3*y
sall $4,%edx # edx = 48*y (t4)
addl 16(%ebp),%ecx # ecx = z+t1 (t2)
leal 4(%edx,%eax),%eax # eax = 4+t4+x (t5)
imull %ecx,%eax # eax = t5*t2 (rval)
  Instructions in different order from C code
  Some expressions require multiple instructions
  Some instructions cover multiple expressions
  Get exact same code when compile:
  (x+y+z)*(x+4+48*y)

## Slide 12: Another Example
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 8(%ebp),%eax
xorl 12(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
movl %ebp,%esp
popl %ebp
ret
Body
Set
Up
Finish
movl 8(%ebp),%eax # eax = x
xorl 12(%ebp),%eax # eax = x^y
sarl $17,%eax # eax = t1>>17
andl $8185,%eax # eax = t2 & 8185
y
x
Rtn adr
Old %ebp
%ebp
0
4
8
12
Offset
Stack
•
•
•

## Slide 13: Another Example
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 8(%ebp),%eax
xorl 12(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
movl %ebp,%esp
popl %ebp
ret
Body
Set
Up
Finish
movl 8(%ebp),%eax eax = x
xorl 12(%ebp),%eax eax = x^y (t1)
sarl $17,%eax eax = t1>>17 (t2)
andl $8185,%eax eax = t2 & 8185

## Slide 14: Another Example
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 8(%ebp),%eax
xorl 12(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
movl %ebp,%esp
popl %ebp
ret
Body
Set
Up
Finish
movl 8(%ebp),%eax eax = x
xorl 12(%ebp),%eax eax = x^y (t1)
sarl $17,%eax eax = t1>>17 (t2)
andl $8185,%eax eax = t2 & 8185

## Slide 15: Another Example
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 8(%ebp),%eax
xorl 12(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
movl %ebp,%esp
popl %ebp
ret
Body
Set
Up
Finish
movl 8(%ebp),%eax eax = x
xorl 12(%ebp),%eax eax = x^y (t1)
sarl $17,%eax eax = t1>>17 (t2)
andl $8185,%eax eax = t2 & 8185
213 = 8192, 213 – 7 = 8185
…0010000000000000, …0001111111111001
Notes: The compiler sees that (1 << 13) – 7 is a constant, and just replaces it with the equivalent value (8185) directly in the code – this left-shift and subtraction is computed once at compile-time, rather than every time logical() is called!