## Slide 1: Conditionals and Control Flow
A conditional branch is sufficient to implement most control flow constructs offered in higher level languages
  if (condition) then {...} else {…}
  while (condition) {…}
  do {…} while (condition)
  for (initialization; condition; iterative) {...}
Unconditional branches implement some related control flow constructs
  break, continue
In x86, we’ll refer to branches as “jumps” (either conditional or unconditional)

## Slide 2: Jumping
jX Instructions
  Jump to different part of code depending on condition codes
jX | Condition | Description
jmp | 1 | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jg | ~(SF^OF)&~ZF | Greater (Signed)
jge | ~(SF^OF) | Greater or Equal (Signed)
jl | (SF^OF) | Less (Signed)
jle | (SF^OF)¦ZF | Less or Equal (Signed)
ja | ~CF&~ZF | Above (unsigned)
jb | CF | Below (unsigned)

## Slide 3: Processor State (IA32, Partial)
Information about currently executing program
  Temporary data ( %eax, …)
  Location of runtime stack ( %ebp,%esp)
  Location of current code control point ( %eip )
  Status of recent tests ( CF,ZF,SF,OF )
%eip
General purpose
registers
Current stack top
Current stack frame
Instruction pointer
CF
ZF
SF
OF
Condition codes
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp

## Slide 4: Condition Codes (Implicit Setting)
Single-bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
Implicitly set (think of it as side effect) by arithmetic operations
  Example: addl/addq Src,Dest ↔ t = a+b
  CF set if carry out from most significant bit (unsigned overflow)
  ZF set if t == 0
  SF set if t < 0 (as signed)
  OF set if two’s complement (signed) overflow (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
Not set by lea instruction (beware!)
Full documentation (IA32): http://www.jegerlehner.ch/intel/IntelCodeTable.pdf

## Slide 5: Condition Codes (Explicit Setting: Compare)
Single-bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
Explicit Setting by Compare Instruction
  cmpl/cmpq Src2,Src1
  cmpl b,a like computing a-b without setting destination
  CF set if carry out from most significant bit (used for unsigned comparisons)
  ZF set if a == b
  SF set if (a-b) < 0 (as signed)
  OF set if two’s complement (signed) overflow (a>0 && b<0 && (a-b)<0) || (a<0 && b>0 && (a-b)>0)
Notes: Src2 can be register, memory, or immediate; Src1 can be register or immediate

## Slide 6: Condition Codes (Explicit Setting: Test)
Single-bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
Explicit Setting by Test instruction
  testl/testq Src2,Src1 testl b,a like computing a & b without setting destination
    Sets condition codes based on value of Src1 & Src2
    Useful to have one of the operands be a mask
  ZF set if a&b == 0
  SF set if a&b < 0
  testl %eax, %eax
    Sets SF and ZF, check if eax is +,0,-

## Slide 7: Reading Condition Codes
SetX Instructions
  Set a single byte to 0 or 1 based on combinations of condition codes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (Signed)
setge | ~(SF^OF) | Greater or Equal (Signed)
setl | (SF^OF) | Less (Signed)
setle | (SF^OF)¦ZF | Less or Equal (Signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 8: Reading Condition Codes (Cont.)
SetX Instructions: Set single byte to 0 or 1 based on combination of condition codes
One of 8 addressable byte registers
  Does not alter remaining 3 bytes
  Typically use movzbl to finish job
int gt (int x, int y)
{
return x > y;
}
movl 12(%ebp),%eax # eax = y
cmpl %eax,8(%ebp) # Compare x : y
setg %al # al = x > y
movzbl %al,%eax # Zero rest of %eax
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
%al
%ah
%cl
%ch
%dl
%dh
%bl
%bh
What does each of these instructions do?
Body: y at 12(%ebp), x at 8(%ebp)
Notes: The order of the cmpl operands is backwards, unfortunately; first we do cmpl y, x, but then the setg is “true” if x > y. So, think of the cmpl as performing x – y, like a sub instruction, and then it makes more sense.

## Slide 9: Reading Condition Codes (Cont.)
SetX Instructions: Set single byte to 0 or 1 based on combination of condition codes
One of 8 addressable byte registers
  Does not alter remaining 3 bytes
  Typically use movzbl to finish job
int gt (int x, int y)
{
return x > y;
}
movl 12(%ebp),%eax # eax = y
cmpl %eax,8(%ebp) # Compare x and y
setg %al # al = x > y
movzbl %al,%eax # Zero rest of %eax
(x – y)
Body: y at 12(%ebp), x at 8(%ebp)
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
%al
%ah
%cl
%ch
%dl
%dh
%bl
%bh