## Slide 1: Section 5: Arrays & Other Data Structures
Array allocation and access in memory
Multi-dimensional or nested arrays
Multi-level arrays
Other structures in memory
Data structures and alignment

## Slide 2: Structures & Alignment
Unaligned Data
Aligned Data
  Primitive data type requires K bytes
  Address must be multiple of K
c
i[0]
i[1]
v
3 bytes
4 bytes
p+0
p+4
p+8
p+16
p+24
Multiple of 4
Multiple of 8
Multiple of 8
Multiple of 8
c
i[0]
i[1]
v
p
p+1
p+5
p+9
p+17
struct S1 {
char c;
int i[2];
double v;
} *p;
Notes: struct S1 { … } *p; - this defines a new type “struct S1”, and creates a variable p with type “struct S1 *”

## Slide 3: Alignment Principles
Aligned Data
  Primitive data type requires K bytes
  Address must be multiple of K
Aligned data is required on some machines; it is advised on IA32
  Treated differently by IA32 Linux, x86-64 Linux, and Windows!
What is the motivation for alignment?

## Slide 4: Alignment Principles
Aligned Data
  Primitive data type requires K bytes
  Address must be multiple of K
Aligned data is required on some machines; it is advised on IA32
  Treated differently by IA32 Linux, x86-64 Linux, and Windows!
Motivation for Aligning Data
  Physical memory is accessed by aligned chunks of 4 or 8 bytes (system-dependent)
    Inefficient to load or store datum that spans quad word boundaries
  Also, virtual memory is very tricky when datum spans two pages (later…)
Compiler
  Inserts padding in structure to ensure correct alignment of fields
  sizeof() should be used to get true size of structs

## Slide 5: Specific Cases of Alignment (IA32)
1 byte: char, …
  no restrictions on address
2 bytes: short, …
  lowest 1 bit of address must be 02
4 bytes: int, float, char *, …
  lowest 2 bits of address must be 002
8 bytes: double, …
  Windows (and most other OSs & instruction sets): lowest 3 bits 0002
  Linux: lowest 2 bits of address must be 002
    i.e., treated the same as a 4-byte primitive data type
12 bytes: long double
  Windows, Linux: lowest 2 bits of address must be 002

## Slide 6: Satisfying Alignment with Structures
struct S1 {
char c;
int i[2];
double v;
} *p1;
Within structure:
  Must satisfy every member’s alignment requirement
Overall structure placement
  Each structure has alignment requirement K
    K = Largest alignment of any element
  Initial address & structure length must be multiples of K
Example (under Windows or x86-64): K = ?
  K = 8, due to double member
c
i[0]
i[1]
v
3 bytes
4 bytes
p1+0
p1+4
p1+8
p1+16
p1+24
Multiple of 4
Multiple of 8
Multiple of 8
Multiple of 8

## Slide 7: Different Alignment Conventions
IA32 Windows or x86-64:
  K = 8, due to double member
IA32 Linux: K = ?
  K = 4; double aligned like a 4-byte data type
c
i[0]
i[1]
v
3 bytes
4 bytes
p1+0
p1+4
p1+8
p1+16
p1+24
c
i[0]
i[1]
v
3 bytes
p1+0
p1+4
p1+8
p1+12
p1+20
struct S1 {
char c;
int i[2];
double v;
} *p1;

## Slide 8: Saving Space
Put large data types first:
Effect (example x86-64, both have K=8)
c
i[0]
i[1]
v
3 bytes
4 bytes
p1+0
p1+4
p1+8
p1+16
p1+24
struct S1 {
char c;
int i[2];
double v;
} *p1;
struct S2 {
double v;
int i[2];
char c;
} *p2;
c
i[0]
i[1]
v
p2+0
p2+8
p2+16
Unfortunately, doesn’t satisfy requirement that struct’s total size is a multiple of K

## Slide 9: Arrays of Structures
Satisfy alignment requirement for every element
struct S2 {
double v;
int i[2];
char c;
} a[10];
c
i[0]
i[1]
v
a+24
a+32
a+40
a[0]
a+0
a[1]
a[2]
a+24
a+48
a+72
• • •
7 bytes
a+48
Notes: struct S2 { … } a[10]; - declares a new type “struct S2”, then declares an array a that contains 10 “struct S2” elements

## Slide 10: Accessing Array Elements
Compute array offset 12i (sizeof(S3))
Element j is at offset 8 within structure
Since a is static array, assembler gives offset a+8
// Global:
struct S3 {
short i;
float v;
short j;
} a[10];
i
j
v
a+12i
a+12i+8
2 bytes
2 bytes
a[0]
a+0
a[i]
a+12i
• • •
• • •
short get_j(int idx)
{
return a[idx].j;
// return (a + idx)->j;
}
# %eax = idx
leal (%eax,%eax,2),%eax # 3*idx
movswl a+8(,%eax,4),%eax # a+12*idx+8
Notes: a + 8: because array a is global, it doesn’t go on the stack – it goes somewhere in the global (static) region of memory. The compiler/assembler doesn’t know where it goes in advance, but will be known when program is loaded. So, the assembler says “hey, when the program is loaded, replace a + 8 with the constant / immediate address that’s equal to the address of a plus 8” – this avoids an extra add for the 8 offset.