## Slide 1: Control Flow
Processors do only one thing:
  From startup to shutdown, a CPU simply reads and executes (interprets) a sequence of instructions, one at a time
  This sequence is the CPU’s control flow (or flow of control)
<startup>
inst1
inst2
inst3
…
instn
<shutdown>
Physical control flow
time

## Slide 2: Altering the Control Flow
Up to now: two ways to change control flow:
  Jumps (conditional and unconditional)
  Call and return
  Both react to changes in program state
Processor also needs to react to changes in system state
  user hits “Ctrl-C” at the keyboard
  user clicks on a different application’s window on the screen
  data arrives from a disk or a network adapter
  instruction divides by zero
  system timer expires
Can jumps and procedure calls achieve this?
  Jumps and calls are not sufficient – the system needs mechanisms for “exceptional” control flow!

## Slide 3: Exceptions
An exception is transfer of control to the operating system (OS) in response to some event (i.e., change in processor state)
Examples: div by 0, page fault, I/O request completes, Ctrl-C
How does the system know where to jump to in the OS?
User Process
OS
exception
exception processing
by exception handler
return to I_current
return to I_next
abort
event
I_current
I_next

## Slide 4: Interrupt Vectors
0
1
2
...
n-1
Each type of event has a unique exception number k
k = index into exception table (a.k.a. interrupt vector)
Handler k is called each time exception k occurs
Exception
Table
code for
exception handler 0
code for
exception handler 1
code for
exception handler 2
code for
exception handler n-1
...
Exception
numbers
Notes: (Jump tables for switch statements: x86 Programming III slides)

## Slide 5: Asynchronous Exceptions (Interrupts)
Caused by events external to the processor
  Indicated by setting the processor’s interrupt pin(s)
  Handler returns to “next” instruction
Examples:
  I/O interrupts
    hitting Ctrl-C on the keyboard
    clicking a mouse button or tapping a touchscreen
    arrival of a packet from a network
    arrival of data from a disk
  Hard reset interrupt
    hitting the reset button on front panel
  Soft reset interrupt
    hitting Ctrl-Alt-Delete on a PC

## Slide 6: Synchronous Exceptions
Caused by events that occur as a result of executing an instruction:
  Traps
    Intentional: transfer control to OS to perform some function
    Examples: system calls, breakpoint traps, special instructions
    Returns control to “next” instruction
  Faults
    Unintentional but possibly recoverable
    Examples: page faults (recoverable), segment protection faults (unrecoverable), integer divide-by-zero exceptions (unrecoverable)
    Either re-executes faulting (“current”) instruction or aborts
  Aborts
    Unintentional and unrecoverable
    Examples: parity error, machine check
    Aborts current program

## Slide 7: Trap Example: Opening File
User calls: open(filename, options)
Function open executes system call instruction int
OS must find or create file, get it ready for reading or writing
Returns integer file descriptor
0804d070 <__libc_open>:
. . .
804d082: cd 80 int $0x80
804d084: 5b pop %ebx
. . .
User Process
OS
exception
open file
returns
int
pop
Notes: Note: on x86-64, syscall and sysret are used instead of int 0x80.
Interrupt number 0x80 tells OS that this is a system call; to specify which system call, the system call’s number is stored in a register (%eax on IA32 Linux) before executing the int instruction.
http://stackoverflow.com/questions/2705702/x86-assembly-before-making-a-system-call-on-linux-should-you-save-all-registers

## Slide 8: Fault Example: Page Fault
User writes to memory location
That portion (page) of user’s memory is currently on disk
Page handler must load page into physical memory
Returns to faulting instruction: mov is executed again!
Successful on second try
int a[1000];
main ()
{
a[500] = 13;
}
80483b7: c7 05 10 9d 04 08 0d movl $0xd,0x8049d10
User Process
OS
exception: page fault
Create page and
load into memory
returns
movl

## Slide 9: Fault Example: Invalid Memory Reference
Page handler detects invalid address
Sends SIGSEGV signal to user process
User process exits with “segmentation fault”
int a[1000];
main ()
{
a[5000] = 13;
}
80483b7: c7 05 60 e3 04 08 0d movl $0xd,0x804e360
User Process
OS
exception: page fault
detect invalid address
movl
signal process
Notes: Can SIGSEGV ever be handled without aborting? Yes, but program can’t really run afterwards: http://www.linuxprogrammingblog.com/all-about-linux-signals?page=4

## Slide 10: Summary
Exceptions
  Events that require non-standard control flow
  Generated externally (interrupts) or internally (traps and faults)
  After an exception is handled, one of three things may happen:
    Re-execute the current instruction
    Resume execution with the next instruction
    Abort the process that caused the exception